# Efficiency Comparison Paper

## ECE445 – Winter 2011

## Portland State University

Tuan Tran Trong

David Rusnac

Dat Nguyen
Introduction:

Circuits that have a voltage conversion ratio of M(D) = D all step down voltages and our task is to find a way to compare these different converters to be able to pick the most efficient one.  When working with an ideal converter circuit, the voltage conversion ratio V/Vg can be found. In this case all circuits will have a conversion ratio of V/Vg = D which is a step down converter. When doing the same analysis with non-ideal components, the same conversion ratio will be found, but with an additional factor. This factor will be the efficiency of the circuit. An efficiency analysis was done for all converters that had a conversion ratio of D and we limited our analysis to only converters that had two switches and at most 2 inductors and capacitors. Only inductor losses were accounted for and switching losses were neglected.

# Part 1: Summary

| Converter | Efficiency ( ) |
| --- | --- |
| A1 |  |
| C1 |  |
| D4 |  |
| D6 |  |
| E2 |  |
| E5 |  |
| F1 |  |
| F3 |  |

## Conclusion:

Based on the results, two distinctions come to light. The first is that A1 has only 1 inductor so in most cases; this circuit will be most efficient because of less inductor losses. The second observation can be made that not all of the converter’s efficiency depend on the duty cycle. Their efficiency will be constant with any duty cycle where as the rest of the circuits will vary based on duty cycle. This is most easily viewed in graphical form. If R1 and R2 are assumed to be similar in resistance value, and the load resistance is significantly larger that both R1 and R2, we can plot efficiencies against duty cycle.

From this graph we can see that in the most general case A1 will be the most efficient due to it lack of second inductor but if we compare only converters that have 2 inductors we see that C1 will be the most efficient converter. Converter D4 is more efficient at higher duty cycles but we see at lower duty cycles it’s efficiency drops off significantly.

In general we can conclude that if there is no preference to complexity, A1 will be the most efficient converter but when comparing the converters with 2 switches and two inductors C1 will provide on average the greatest efficiency of the discussed converters.

# Part II: Analysis

A1 Efficiency Analysis: S2: M=D

For Time Interval DTs

Inductor Voltage

Capacitor Current

For Time Interval DTs

Inductor Voltage

Capacitor Current

Volt-Second Balance

I is substituted in from average capacitor current

C1 Efficiency Analysis: S2: M=D

For Time Interval DTs

L2 average voltage

For DC:

No DC current through C1 or C2

For Time Interval DTs

L2 Average Voltage

No DC current through C1 and C2

Volt-second balance for Inductor L2:

D4 Efficiency Analysis: S1: M=D

For Time Interval DTs

Inductor Voltages

Capacitor Currents

For Time Interval D’Ts

Inductor Voltages

Capacitor Currents

Volt-Second Balance for L2:

Charge balance for C1:

Charge balance for C2

Substituting Currents back into charge balance equation

D6 Efficiency Analysis: S2: M=D

+	-
          VL2

+	-
     VL1

I1

+ 

     V1

-

I2

+ 

     V2

-

V

DTs:

I1

+          -
     VL1

+ 
     V1

-

+ 
     V2

-

+          -
     VL2

I2

V

+          -
     VL1

I1

D’Ts:

+          -
     VL2

I2

V

+ 
     V2

-

+ 
     V1

-

Volt-second balance:

Charge balance:

I1 I1 I2 V E2 Efficiency Analysis: S2: M = D

I1

DTs:

V

+

-

I2

+  V1  -

+ VL2  -

+ VL1  -

D’Ts:

Volt-second balance:

Charge balance:

E5 Efficiency Analysis: S1: M = D

DTs:

DTs:

Charge balance on  C1, C2:

Volt-second on L1, L2:

F1 Efficiency Analysis: S2: M=D

For Time Interval DTs

Inductor Voltages

Capacitor Currents

For Time Interval D’Ts

Inductor Voltages

Capacitor Currents

Average Inductor Voltage for L1:

Average Inductor Voltage for L2:

Charge balance for C1:

Charge balance for C2

Substituting I1 and I2

Substituting Currents back into volt-second balance equations

F3 Efficiency Analysis: S1: M=D

For Time Interval DTs

Inductor Voltages

Capacitor Currents

For Time Interval D’Ts

Inductor Voltages

Capacitor Currents

Average Inductor Voltage for L1:

Average Inductor Voltage for L2:

Charge balance for C1:

Charge balance for C2

Substituting I1 and I2

Substituting Currents back into volt-second balance equations